## Slide 1
Mock Project - MCU
Team 2

## Slide 2
Our Team
SonLD14
DangNTH3
HuyNV37
DungLM7
CuongNQ26
NamNH123

## Slide 3
Used to load and start your Application
Boot program
Use Button to switch firmwares
With two memory location on Flash memory
Firmware 1: Blink led
Firmware 2: Read ADC
Two firmwares
Requirement
Design and Implement an application using Bootloader

## Slide 4
Introduction to Bootloader

## Slide 5
What is Bootloader?
A bootloader is an application whose primary objective is to upgrade/modify system software without the intervention of specialized firmware upgrade tools. Bootloaders can have many functionalities, but it's mainly used to manage the application.

## Slide 6
How it works
Bootloader
Application
Reset

## Slide 7
Why do we need to use it?
Update Firmware
Easy to update firmware remotely via wireless network
Security
Easy to use code to check firmware before loading it to avoid hackers

## Slide 8
Project Design

## Slide 9
Project Design
Bootloader Handle
Main Application
Backup Application
Receive and Parse SREC Data
Project

## Slide 10
Coding Structure
Main
Middleware
Driver

## Slide 11
Bootloader
Write firmwares into the memory
After reset, PC jumps to Bootloader Firmware
+ Press Button SW1, the program jumps to Main Application
+ Press Button SW2, the program jumps to Backup Application
…
Backup
Main
…
…
Bootloader
0x0000.0000
0x0003.E.800
0x0003.B000
Backup
Bootloader
Main
Reset
Click SW1
Click SW2

## Slide 12
Bootloader
How to build a Boatloader program

## Slide 13
Firmware 1 – Main Application
Blink Led by using Button (External Interrupt)
Press Button SW1: Both LED1 and LED2 blink with the cycle T = 200ms
Press Button SW2: LED1 and LED2 blink one after another with the cycle T = 100ms
KL46 MCU
Button
LED2
LED1

## Slide 14
Firmware 2 - Backup
Read Light Sensor by using ADC
KL46 MCU
PC
Light Sensor
0x55
10 times of data
Send a command (0x55) from PC to MCU, get 10 values of sensor.

## Slide 15
SREC file format
Receive and Parse SREC
SREC file format
Output

## Slide 16
Receive and Parse SREC
Modify *icf file
Output Data
An SREC file with a new address
Procedure to get output data of each application
Rebuild All
Parse SREC

## Slide 17
Run
&
Result

## Slide 18
Work Evaluation
Member | Work Assigment | Grade
Cường | SREC, Timer, Slide | 3
Dũng | UART, Main, Presentation | 2
Đăng | Driver, Clock, Main | 5
Huy | SREC, Flash, Main | 5
Sơn | Firmware 2, Main | 4
Nam | Firmware 1, Button | 1
5: Very good
4: Good
3: Complete
2. Incomplete
1. Bad

## Slide 19
Đội ngũ của chúng tôi
THÙY DUNG
Giám đốc Điều hành
LÊ BÍCH NHƯ
Giám đốc Vận hành
PHẠM HỮU TRỌNG
Giám đốc Sản phẩm